## Slide 1
Rebar Rebels
Mech - ARE
Software
AI-Based Campus Structural Health Monitoring System
STHIRA : Structural Health Inspector & Risk Assessment

## Slide 2
STHIRA: measuring cracks to the millimetre with just a smartphone
Why campus audits fall short
Visual inspections happen once every 3–5 years, and they can't tell harmless plaster shrinkage from a serious shear crack.
NDT equipment costs ₹2,00,000 or more. Ordinary AI crack detectors struggle too, because a photo has no sense of scale: a 0.2 mm hairline crack can look like a 3 mm one when zoomed in.
Our solution (software only, scoped for a 10-hour build)
1. Scale from a marker. A printed 5 cm ArUco sticker, or a normal 85.6 mm college ID card, corrects camera tilt and gives an exact mm-per-pixel scale. No extra hardware.
2. Width along the whole crack. We thin the crack to a 1-pixel line and use the Euclidean Distance Transform (EDT) to read its width in mm at every point. The crack angle (PCA) flags dangerous 45° shear cracks.
3. Coin-tap sound test (ASTM D4580). The phone mic records a ₹5 coin tap at 48 kHz, and an FFT shows hidden voids: below 900 Hz is hollow, above 1,400 Hz is solid concrete.
4. IS 456:2000 and CPWD costing. Results go into a Building Health Index on a campus map, with a repair Bill of Quantities in ₹.
1. Capture: crack photo with ArUco marker + 3 s coin-tap audio
2. Preprocess (OpenCV): remove shadows, set exact mm/px scale
3. Analyse: crack width heatmap + audio FFT
4. Report: IS 456 check, health score, campus map, repair cost (₹)
Sample crack photos (stock images)

## Slide 3
Input: phone camera, ArUco / ID-card marker, 48 kHz mic (.WAV tap)
Preprocessing (OpenCV): CLAHE in LAB colour to remove shadows, 3x3 perspective warp
Analysis: YOLOv8-Seg / adaptive mask, 1-px skeleton + EDT width, SciPy FFT spectrum
Output (Streamlit + Folium): campus health map, IS 456 alert, CPWD cost PDF
The maths behind it
Scale (mm/px) = marker width (50 mm) ÷ marker width in the warped image (px)
Crack width W(x,y) = 2 × EDT(skeleton pixel) × scale
Crack angle α comes from PCA on the skeleton. 30°–60° is treated as diagonal shear.
Audio: a dominant FFT peak above 1,400 Hz suggests solid concrete, below 900 Hz an internal void. These are starting thresholds, to be tuned on campus samples.
Data and sources
Images: Crack500 (pixel masks) to fine-tune YOLOv8-Seg, SDNET2018 for crack / no-crack checks, plus campus photos we will collect with ArUco markers.
Audio: 48 kHz .wav coin-tap recordings we will record on solid concrete columns and on hollow panels.
Standards: IS 456:2000 crack width limits (0.1–0.3 mm) and CPWD DSR repair rates.
Python 3.10 & Streamlit
Web UI and backend in one
OpenCV (cv2.aruco)
Homography and CLAHE
YOLOv8-Seg & scikit-learn
Crack mask and PCA crack angle
SciPy (edt & fft)
Sub-mm width and audio spectrum
Folium / Leaflet.js
Interactive campus health map
SQLite & ReportLab
Audit history and CPWD BoQ PDF

## Slide 4
Feature / Problem | Conventional Civil Audit | Basic AI Classifier | STHIRA (Ours)
Hardware cost | ₹50,000 – ₹2,50,000+ rigs | ₹0 (phone camera) | ₹0 (phone + ArUco / ID card + ₹5 coin)
Camera distance bias | Manual plastic scale card | Fails: no physical scale | Marker + 3x3 homography give true mm/px
Curved crack width | Judged by eye | Fails: bounding box error | 1-px skeleton + EDT heatmap
Hidden internal voids | Destructive core drilling | Fails: surface photo only | 48 kHz coin-tap FFT
How we handle the hard cases
1. Shadows and glare in corridors. We apply CLAHE in LAB colour space before segmentation, so shadows aren't mistaken for cracks.
2. Plaster vs. structural cracks. If the visible crack is over 0.3 mm but the coin-tap FFT is above 1,400 Hz (solid) and the angle is outside 30°–60°, it is marked as surface plaster spalling. This avoids false alarms.
3. Noise during the tap test. A 600 Hz high-pass filter and a 50 ms window around the tap peak pick out the coin and ignore speech.
4. Doable in 10 hours. Pure Python and Streamlit, no custom hardware, no multi-day GPU training.
How the rule engine labels a crack
Crack | Tap sound | Verdict
Angle 30°–60° | Any | Shear risk: inspect first
> 0.3 mm | < 900 Hz | Void risk: inspect
> 0.3 mm | > 1,400 Hz | Plaster spalling: cosmetic
0.1–0.3 mm | > 1,400 Hz | Minor: seal and monitor
< 0.1 mm | > 1,400 Hz | Hairline shrinkage: no action
Thresholds start from IS 456 and ASTM D4580 and get tuned on campus samples.

## Slide 5
Impact
Students and staff become the sensors. 5,000+ people already carry a smartphone, so there is no hardware to buy.
Lower audit costs. Harmless hairline shrinkage cracks (under 0.1 mm) are filtered out, so the Estate Office calls structural consultants only for real defects. Audit effort goes only where it is needed.
Repair budgets in rupees. The Bill of Quantities compares options such as epoxy injection grouting and polymer mortar plastering, using CPWD DSR rates.
Safer buildings. IS 456:2000 limits are used to flag 45° shear cracks and ceiling delamination before they turn into accidents.
Where this goes next
Phase 2, tracking crack growth. Photos taken months apart are aligned with ORB feature matching to give crack growth speed in mm/month.
Phase 3, high ceilings without a marker. Monocular depth (Depth Anything V2) plus the phone's gyroscope tilt angle (θ) lets us measure cracks on 30-ft auditorium ceilings without stickers.
Phase 4, drones and city scale. Run the same pipeline on campus inspection drones and on municipal bridge and housing portals.
Phase 1 (Hackathon MVP): ArUco + EDT + coin-tap FFT
Phase 2: ORB temporal diff + depth AI
Phase 3: drone swarm & smart-city twin

## Slide 6
Codes and standards
Datasets and papers
1. IS 456:2000 (Bureau of Indian Standards). Plain and Reinforced Concrete – Code of Practice, Clause 35.3.2. Permissible surface crack width: 0.3 mm for mild exposure, 0.2 mm moderate, 0.1 mm severe.
2. ASTM D4580 (acoustic sounding). Standard Practice for Measuring Delaminations in Concrete Bridge Decks by Sounding, the basis for our coin-tap method.
3. CPWD Handbook & DSR (Central Public Works Dept). Handbook on Repair and Rehabilitation of RCC Buildings and the Delhi Schedule of Rates, used for the automated repair estimate.
4. Crack500 & DeepCrack. Yang et al., "Feature Pyramid and Hierarchical Boosting Network for Pavement Crack Detection", IEEE Transactions on Intelligent Transportation Systems.
5. SDNET2018. Dorafshan et al., "SDNET2018: An annotated image dataset for non-contact concrete crack detection using deep CNNs", Data in Brief (230,000+ images).
6. OpenCV ArUco calibration. Garrido-Jurado et al., "Automatic generation and detection of highly reliable fiducial markers under occlusion", Pattern Recognition.

## Slide 7
Aniket Singh | 260901 | aniketsingh_260901@aitpune.edu.in
Harshul Singal | 260942 | harshulsingal_260942@aitpune.edu.in
Mahima Khedar | 260956 | mahimakhedar_260956@aitpune.edu.in
Neeraj Kumar | 261093 | neerajkumar_261093@aitpune.edu.in